## Slide 1: Electrical Principles & Technologies
Unit D
Redding 2016

## Slide 2: Topic 1 - Electric Charges
Producing Charges
Materials that attract or repel other materials are said to be charged, or carry an electric charge. Charges, which can be detected by an electroscope, are produced when materials are rubbed, touched or moved together and then separated.
To refer to charges as stationary or ‘static’, would be inaccurate, because the charges are moving. ‘Unbalanced charges’ is a more accurate way of describing this electricity. The quantity of electric charge is measured in coulombs.
Notes: When you get a 'shock', feel a 'jolt', or, a 'spark', you are experiencing the same type of electrical effect that makes lightning. Static electricity happens when there is an imbalance of electrons (which have negative charges).

## Slide 3: Topic 1 - Electric Charges
Making Sense of Electrical Charges
Most objects have the same number of positive (proton) and negative (electron) charges. This makes them neutral (no charge). When there is a difference in the electrical charge, certain actions are predictable, because of the Laws of Electrical Charges.
Notes: Benjamin Franklin was the first to describe the charges as ‘positive’ or ‘negative’. When amber is rubbed with fur - some of the electrons in the fur move to the amber - the amber becomes negatively charged and the fur is positively charged.

## Slide 4: Topic 1 - Electric Charges
Conductors, Insulators, and In-Between
In insulators electrons are bonded closely to the nuclei, while in conductors, the electrons are free to move easily.
Most metals are conductors and non-metals are insulators.
A special type of conductor, called a resistor allows electrons to flow, but provides some resistance.
Semiconductors are almost perfect conductors - they have almost no resistance to electron flow. Silicon semiconductors are used extensively to make computer microchips.
  The largest obstacle is to get the semiconductor to work at reasonable temperatures for practical applications. Superconductors are materials that offer little, if any, resistance to the flow of electrons.

## Slide 5: Topic 1 - Electric Charges
Neutralizing Unbalanced Charges
Electrical Discharge is the movement of charges whenever an imbalance of charges occurs. The action results in neutralizing the objects. The over-charged electrons repel the electrons in the object and the positive protons attract the charged electrons causing a discharge or 'miniature lightning bolt'. There is now an electron balance. An ionizer can be used to neutralize charges on non-conductors.
Preventing Electrostatic Buildup
‘Static cling’ is a build-up of unbalanced charges on different materials. This build-up can be very costly because of the damage it can cause.
Anti-static materials have to be used when handling charged objects, so that a discharge (which could cause harm or damage) does not occur. Anti-static sprays, coating or grounding strips.

## Slide 6: Topic 2 - Electricity Within a Circuit
Circuit Elements and Diagrams
A circuit is a pathway that allows the flow of electricity. Most electrical circuits use wires (as conductors), although others may use gases, other fluids or materials. All circuit diagrams have four basic parts:
• source - provides energy and a supply of electrons for the circuit … Battery
• conductor - provides a path for the current …Wires
• switching mechanism - controls the current flow, turning it off and on, or directing it to different parts of the circuit …Switch
• load - converts electrical energy into another form of energy … Bulb

## Slide 7: Electricity Within a Circuit
A drawing made with these symbols is called a schematic or schematic diagram.
The rules to follow when making schematic diagrams:
Use a pencil and ruler on graph or unlined paper
Place the components in a rectangular or square arrangement
Conducting lines should be straight with ‘right-angled’ corners
Do not cross conductors
Be neat and make the sizes of the symbols consistent and easy to see

## Slide 8: Electricity Within a Circuit
Measuring Current
The steady flow of charged particles is called electrical current. The flow continues until the energy source is used up, or disconnected. The rate at which an electrical current flows is measured in amperes (A).
This flow varies from a fraction of an ampere to many thousands of amperes, depending on the device. An instrument used to measure very weak electric current is called a galvanometer. Larger currents are measured with an ammeter.

## Slide 9: Electricity Within a Circuit
Measuring Voltage
Electrical energy is the energy carried by charged particles. Voltage is a measure of how much electrical energy each charged particle carries.
Also called 'potential difference', the energy delivered by a flow of charged particles is equal to the voltage times the number of particles. Voltage units are volts (V).
A simple way to measure voltage is with a voltmeter. [red to positive (+) and black to negative (-)]

## Slide 10: Electricity Within a Circuit
Rivers of Electricity
Electric circuits are often compared to water systems. Electric charge is like the water, as it flows (input) it makes changes in the energy that results (output). Microcircuits (Integrated Circuits) - transistors are used with three layers of specially treated silicon, with the middle layer (receiving a small voltage, allowing it to control the voltage in the outer layers, allowing them to act as switches.
Microcircuits are made up of transistors and resistors and are built on an extremely small scale. Integrated circuits put all of the components in one chip, reducing the size of the circuit.

## Slide 11: Topic 3 - Resisting the Movement of Charge
Resistance is a measure of how difficult it is for the electrons to flow through a conductor. Resistance also converts electric energy into other forms of energy.
Generally, it can be said that conductors have low resistance and insulators have high resistance. The standard unit for resistance is ohm (Ώ).
Resistance can be measured directly with an ohmmeter, but a multi-meter is used more often to measure resistance.

## Slide 12: Topic 3 - Resisting the Movement of Charge
Calculating Resistance
Electrical resistance is calculated by finding the ratio of the voltage across the load (V) to the current through the load (I). This is called
Ohm’s Law. R = V / I
The more resistance a substance has, the greater the energy gain it receives from the electrons that pass through it. Solutions can also be resistors. 'Lie detectors' are also special applications of resistance within the body (skin resistance, blood pressure and respiration). An increase in stress (usually associated with a lie) will improve conductivity and show a 'peak' in the recording device.
If the temperature of a resistor changes, the resistance changes as well (resistance is usually low when the resistor is cool, and as the temperature increases, so does resistance).

## Slide 13: Resisting the Movement of Charge
Model Problem - Applying Ohm's Law - Sample textbook problems p. 282
Resistors Different resistors are used for different applications, especially in electronics. There are many styles, sizes and shapes. The major application for resistors is to control current or voltage to suit the specific needs of other electrical devices within the same circuit. The two most common resistors are the wire-wound and carbon-composition types. The colored strips on a resistor usually indicate the level of resistance and quality.

## Slide 14: Resisting the Movement of Charge
Types of Circuits
A series circuit provides only one path for the current to flow.
A parallel circuit provides multiple pathways.

## Slide 15: Resisting the Movement of Charge
House Wiring
Practical wiring in the home uses parallel circuits. The voltage across each load is the same, and by turning on one appliance in the circuit, the energy will not be reduce to the other devices.
Caution – current through wires connected to the source increases whenever another branch in the circuit is closed.
Factors that affect the Resistance of Wire
Factor Effect
Length - Resistance increases with length
Cross-section area - Resistance decreases with area (gauge – AWG #)
Temperature - As temperature increases, resistance increases
Material - Determined by the structure of the atoms

## Slide 16: Topic 4 - The Energy Connection
The scientific definition of energy is ‘the ability to do work’.
The four most common forms of energy are:
• chemical - potential or stored energy stored in chemicals, released when the chemicals react.
• electrical - energy of charged particles, transferred when they travel from place to place.
• mechanical - energy possessed by an object because of its motion or its potential to move.
• thermal - kinetic energy of a substance

## Slide 17: Topic 4 - The Energy Connection
Electricity and Heat
A thermocouple is a device that can convert thermal energy into electrical energy. It consists of two different metals (bimetal) joined together that conduct heat at slightly different rates. When heated, the difference in conduction results in electricity flowing from one metal to the other.
Thermocouples are useful for measuring temperatures in areas that are difficult to access or too hot for a regular liquid-filled thermometer. Ovens and heaters do the opposite. They convert electrical energy into thermal energy.
A thermo-electric generator is a device based on a thermocouple that converts heat directly into electricity without moving parts. Several thermocouples connected in a series is called a thermopile. Thermopiles are extremely reliable, low-maintenance devices and are often used in remote locations for emergency power generation.

## Slide 18: Topic 4 - The Energy Connection
Electricity to Motion
The piezoelectric effect produces sound by converting electricity into motion (vibrations). When a piezoelectric crystal, such as quartz, or Rochelle salt is connected to a potential difference, the crystal expands or contracts slightly. Material touching the crystal experiences pressure, creating sound waves or vibrations.
Motion to Electricity
A barbeque spark lighter uses the piezoelectric effect in reverse. When a crystal or Rochelle salt is compressed or pulled, a potential difference is built up on the opposite sides of the crystal. Conductors then take this through a circuit to produce electric energy (a spark).
Electricity to Light
An incandescent resistance filament (load) glows white-hot when electricity is passed through it. In fluorescent tubes a gas glows brightly and when crystals are struck together they can produce light. LED’s (light-emitting diodes) are solid –state components that use a fraction of the power. When connected to a semiconductor chip in the right direction, they will produce light and last for many years.

## Slide 19: Topic 4 - The Energy Connection
Light to Electricity
Solar panels, containing photovoltaic cells can convert light into electrical energy. The photovoltaic (PV) cells, or solar cells, are made of semiconductor materials, such as silicon.
Certain animals, namely, the electric eel, can produce electric shock, to kill or stun prey. They have a special organ that contains specialized muscle cells called electroplaques. Each cell produces a small amount of electricity. When all the cells work together, a large amount of electricity is produce and used to help the eel survive.
Notes: When light is present, the material, breaking electrons loose – allowing them to flow freely, absorbs some. This current is drawn off by metal contacts on the top and bottom of the cell and then used in devices such as calculators, heater, or emergency telephones.

## Slide 20: Topic 5 - Portable Power
Electrochemical Cells
Two metal electrodes are surrounded by an electrolyte. These cells supply a steady current. The chemical reaction in a cell releases free electrons, which travel from the negative terminal of the cell, through the device, which uses the electricity, and back to the positive terminal of the cell. The chemical reactions within the cell determine the potential difference (voltage) that the cell can create. Several cells connected in series produces a higher voltage, and is commonly referred to as a battery, which is a sealed case with only two terminals.
A primary cell is one in which the reactions will not continue after the reactants are used up.
A secondary cell uses chemical reactions, which can be reversed. These are referred to as rechargeable batteries.

## Slide 21: Topic 5 - Portable Power
Wet cells use a liquid electrolyte. Wet cells are 'wet', because the electrolyte is a liquid.
Each electrode (zinc and copper) reacts differently in the electrolyte. The acidic electrolyte eats away the zinc electrode, leaving behind electrons that give it a negative charge.
The copper electrode is positive, but it is not eaten away. Electrons travel from the negative terminal (attached to the zinc electrode) through the device and on to the positive terminal (attached to the copper electrode).
Dry cells –the electricity-producing cells, referred to as 'batteries', are called dry cells, because the chemicals used in them are a paste.
The dry cell is made up of two different metals, called electrodes in an electrolyte. An electrolyte is a paste or liquid that conducts electricity because it contains chemicals that form ions.
The electrolyte reacts with the electrodes, making one electrode positive and the other negative. These electrodes are connected to the terminals.

## Slide 22: Topic 5 - Portable Power
the cell. The reversed flow of electrons restores the reactants in the cell. The most common reactions that are efficient enough to be used for these types of cells are Nickel Oxide and Cadmium (Ni-Cad). The reactants are restored, but the electrodes will eventually wear out over time.
The tiny cells in a pacemaker can last from 5-12 years
Fuel Cells
Fuel cells combine hydrogen and oxygen without combustion. Electricity, heat and pure water are the only by-products of the fuel cell’s reaction. They are 50-85% efficient.
World leader in fuel cell technology is a Canadian company Ballard Power Systems, in Burnaby, B.C.

## Slide 25: Topic 6 - Generators and Motors
A device that converts mechanical energy (energy of motion – windmills, turbines, nuclear power, falling water, or tides) into electrical energy is called an electric generator. The operation of a generator depends on the relationship between electricity and magnetism.
Electricity to Magnetism
Deflection of a compass needle using electrical current showed that there is a relationship between electricity and magnetism. Hans Christian Oersted found that the current created a magnetic field around the wire.
The amount of needle deflection depended on how much electric current was flowing in the wire. When the current was reversed, the needle moved in the opposite direction.

## Slide 26: Topic 6 - Generators and Motors
Electromagnets When a soft iron core is inserted into a coil of wire and a current is passed through the wire, a very strong temporary magnet is produced, called an electromagnet.
The strength of an electromagnet is affected by the …
type and size of core
strength of current
number of coils

## Slide 27: Topic 6 - Generators and Motors
Magnetism to Electricity Electric effects can also be created using a magnet. Michael Faraday (and Joseph Henry) discovered electromagnetic induction in 1831. Moving a conducting wire through a magnetic field by moving it back and forth through the field, Faraday created the first electricity-producing generator, which could generate electrical current.
Faraday introduced terms such as ‘ion’, ‘electrode’, ‘cathode’, and ‘anode’ to science and invented the lines of magnetic force. The farad, a unit for measuring stored electric charge, was named after him.

## Slide 28: Topic 6 - Generators and Motors
What’s in a Generator?
An AC generator – the most common type – has a coil of wire rotating inside a stationary field magnet. The central axle of an AC generator has a loop of wire attached to two slip rings. The current is switched as the loops move up and down alternatively through the magnetic field. The slip rings conduct the alternating current to the circuit through the brushes (the brush and ring assembly allows the whole loop to spin freely).
The electricity produced by this type of generator is called alternating current because it changes direction In large AC generators many loops of wire are wrapped around an large iron core. Massive coils of wire rotating in huge generators can produce enough electricity to power an entire city.

## Slide 29: Topic 6 - Generators and Motors
A DC generator is much the same as a DC motor, and is often called a dynamo. The spinning armature produces the electricity (if electricity is passed through a DC generator, it will spin like a motor).
The armature is connected to a split ring commutator which enables this type of generator to send current through a circuit in only one direction.
The DC generator’s pulsating electricity is produced in one direction - referred to as direct current - and coincides with the spinning of the generator.

## Slide 30: Topic 6 - Generators and Motors
Electric Motors:
Electric to Mechanical Energy An electric motor is constructed in exactly the same way as a generator. Instead of producing electricity, it uses electrical energy to make a wire coil spins between the poles of a magnet.
Current flowing through the coils makes it an electromagnet, which is then affected by the laws of magnetic forces when it is in proximity to the field magnet. Opposite poles attract and like poles repel. All electric motors operate on this principle.

## Slide 31: Topic 6 - Generators and Motors
DC Motors
Faraday constructed the first motor. By coiling (copper) wire around a (iron) metal core a strong electromagnet can be made. When attached to an electrical source it will produce a strong magnetic field. To keep this electromagnet spinning in a magnetic field, the direction that the current is traveling through the coil must be switched. This is accomplished by with a gap, which allows the polarity of the electromagnet change just before it aligns with the permanent magnet.
DC motors use a commutator (a split ring that breaks the flow of electricity for a moment and then reverses the flow in the coil, when the contact is broken, so is the magnetic field) and brushes (contact points with the commutator) to reverse the flow of electricity through the magnetic field. The armature (the rotating shaft with the coil wrapped around it) continues to spin because of momentum, allowing the brushes to come into contact once again with the commutator.

## Slide 32: Topic 6 - Generators and Motors
AC Motors
AC motors have a rotating core, or rotor, made up of a ring of non-magnetic conducting wires connected at the ends and held in a laminated steel cylinder. Surrounding the rotor is a stationary component called a stator. The stator is a two-pole electromagnet. When the motor is turned on, the attraction and repulsion between the poles of the stator and the rotor cause the rotor to spin.

## Slide 33: Topic 7 - Electricity in the Home
Transmission of Electricity through the Power Grid Transformers are used to change the amount of voltage with hardly any energy loss. Voltage change is necessary because the most efficient way to transmit current over long distances is at high voltage and then reduced when it reaches its destination, where it will be used.
A step-up transformer increases voltage at the generating plant prior to distribution to the power grid over high voltage transmission lines, whereas, a step-down transformer reduces voltage just before entering your home.

## Slide 34: Topic 7 - Electricity in the Home
From the Grid into Your Home
Coming in contact with a power transmission line can prove to be deadly. By touching it, a short circuit can occur, because the electricity is trying to find a path to the ground - you can complete the circuit, and it may be fatal. Power needs to enter your home safely. Electrical power enters a meter
on the side of your house where electrical usage is recorded on little dials
Power is then routed into the service panel (usually in the basement).
The main circuit breaker shuts off all the power in the house at once, in case of an overload.
The individual circuit breakers in the service panel control the branch circuits, located throughout the entire house.
Each branch circuit is connected in parallel to wall plugs, lights and wall switches within a particular area of the house.
Each branch circuit is a series of 14 gauge electrical cables that contain:
  2 ‘live’ insulated wires (white – neutral; and black – hot);
  a ‘ground’ wire (bare copper wire, or insulated green).

## Slide 35: Topic 7 - Electricity in the Home
Digital Devices
The four basic elements of a circuit are present in a microcircuit, as well as a normal electrical circuit, although they may be in different forms. Conductors are thin traces of copper, instead of wires. Resistors and lamps are similar, but the switches are very different. To process the digital information switches in microcircuits use ‘binary code’ – 0 and 1 - for on and off.
These electronic digital switches are transistors –
solid state components that are controlled by electronic signals.
The transistors can then control other signals.

## Slide 36: Topic 7 - Electricity in the Home
Measuring Electric Power Power is defined as energy per unit time. Electric power describes the amount of electric energy that is converted into other forms of energy (heat, light, sound, or motion) every second. The formula that is used is:
Power (watts) = Energy (joules) / Time (seconds)
A kilowatt is 1000 watts.
The electrical power formula can be manipulated as follows to determine Power, Current or Voltage use:

## Slide 37: Topic 7 - Electricity in the Home

## Slide 38: Topic 7 - Electricity in the Home
Power Rating The power rating on an energy using device tells you how many joules of energy ( 1 W = 1J/s ) the device uses every second it is on.
ENERGUIDE labels help consumers make comparisons of energy use, when purchasing large appliances.
Measuring energy inputs and energy outputs allows you to calculate the efficiency of devices and systems.

## Slide 39: Topic 7 - Electricity in the Home
Electric Devices and Efficiency
Energy is neither created nor destroyed. It doesn't appear and then disappear, but is transformed from one form to another. Most of the energy transformed in a light bulb is wasted as heat. Known as the Law of Conservation of Energy, no device is able to be 100% efficient in transforming energy. Most often, the energy is lost, or dissipated as heat. Mechanical systems also dissipate energy to their surroundings, but not as obvious as the heat loss. Much of the dissipated energy is sound.
The efficiency of a device is the ratio of the useful energy that comes out of a device to the total energy that went in. The more input energy converted to output energy, the more efficient the device is.
Efficiency ( % ) = useful energy output (J) x 100%
total input energy (J)
Comparing efficiencies of devices by their energy cost and their environmental impact can be an important decision that can affect sustainability of our resources, by helping us to make better consumer choices.

## Slide 40: Topic 7 - Electricity in the Home
Electrical Safety Pointers...
• Cover electrical outlets with child-proof covers if they are within reach of small children
• Don't use devices that have a frayed or exposed power cord
• Always unplug an electrical device before disassembling it
• Don't put anything into an electrical outlet - except a proper plug for an electrical device
• Don't overload an electrical circuit, by trying to operate too many devices at once
• Don’t bypass safety precautions when you are in a hurry
• Pull on the plug, not the wire
• Never remove the third prong from a 3 prong plug
• Never allow yourself to come into contact with anything that is touching live electrical wires.
• Never use ungrounded or frayed 2 prong electrical cords outdoors
• Do not operate electrical equipment outdoors in the rain
• Check before you dig – you could end up digging into electrical cables or wires for communication causing injury and disruption.

## Slide 41: Topic 8 - Electricity Production and the Environment

## Slide 42: Electricity Production & the Environment
Fossil Fuels Affect Land and Air
Coal is mined in Alberta in open pits, which are an eyesore, and disturb topsoil and vegetation. Underground mines produce ‘tailings’ which accumulate near the mine. Water seeps through these tailings and becomes acidic and contaminated. Fossil fuel reserves are decreasing, but with less reliance on these fuels we will be able to see a decrease in pollution. The burning of these fuels creates contaminants such as visible particles and invisible gases (SO2 is one such gas). Electrostatic precipitators can remove most of the solid particles, but not the gases. Sulfur dioxide can be reduced by using scrubbers – which spray a water solution through the gas, making sulfuric acid, which is then collected and sold. Another gas produced is carbon dioxide CO2 which is a greenhouse gas. Producing more of this naturally occurring gas helps the atmosphere trap more heat, leading to global warming. Some generating plants are switching to natural gas which burns a little cleaner. Finding ways to lower our dependence on fossil fuels and finding alternative fuel sources is a decision that will determine much of what our future environment will be like.

## Slide 43: Electricity Production & the Environment
Electric Energy from Flowing Rivers Hydro-electric plants use falling water (gravity), and pressure to generate electricity. Large dams raise the water above the power plant (which is usually built inside the dam), near the base.
A channel, called a penstock, directs the water (at high pressure) to a turbine. The turbine then converts mechanical energy to electrical ener
Although these hydro-electric plants appear to be doing no harm to the environment, the reservoir they have to create behind the dam, destroys habitat and displaces whoever lived in the area prior to the reservoir being created. When the submerged vegetation is decomposed, bacteria take up the oxygen supply in the water, methane gas can be produced, and aquatic species – such as fish, are affected when the oxygen levels drop. Other species take over and a new ecosystem can be created.

## Slide 44: Electricity Production & the Environment
Energy from Atomic Reactions Bombarding uranium atoms with tiny particles, called neutrons cause the uranium to split into two smaller atoms.
This is called nuclear fission.
The process creates a huge amount of energy which is used to generate electricity in a thermonuclear plant.
Heating the Environment
All thermonuclear and thermo-electric-generating plants release thermal energy into the environment. 43% of the water used in the cooling process enters the environment. Thermal pollution occurs when this heated water is not cooled before it re-enters the water system. This overheated water can upset the life cycles of organisms in the water and be fatal because they cannot tolerate the sudden temperature change. The heated water also contains less oxygen. To reduce this type of pollution, plants are required to have holding ponds or towers which hold the water until it returns to normal levels.

## Slide 45: Electricity Production & the Environment
Cogeneration
Cogeneration is the dual generation of electrical and thermal energy. The cogeneration systems usually are associated with industries, or commercial complexes. The cogeneration plant (like Poplar Creek Power Plant in Fort McMurray) provides electricity and heat or steam to the industry and may even sell excess electricity to the provincial power grid.
Renewable resources like these alternative sources of energy can be replenished over and over again. Tree harvesting can also be renewed, but it takes a much longer period of time to renew this resource. They can also negatively affect the environment: Dams, wind farms and solar cell arrays can destroy large areas of ecological habitat; Tidal power plants can disrupt the habitat of fish and other marine life.